## Slide 1: UART
Serial Com

## Slide 2: Outline
Uart introduce
Baud-rate Introduction
Parity Bit Introduction
Uart setting

## Slide 3: Uart(I)
What the UART do on the communication
  UART(Universal Asynchronous Receiver Transmitter)
  all sequence interface transform from Parallel to Serial on transmitter (Tx)
  all sequence interface transform from Serial to Parallel on receiver(Rx)
UART provide some status information
  receiver full or not
  Transmitter empty or not

## Slide 4
Microcontroller
Rx
Tx
User
CPU
Serial input
Parallel output
Serial output
Parallel input
match baud rate
match baud rate
UART
Rx full
Tx empty

## Slide 6: Serial vs Parallel

## Slide 7: Asynchronous vs Synchronous

## Slide 8: Serial port
Baud rate(Speed)
  the unit for symbol rate or modulation rate in symbols per second or pulses per second
Data bits
  Between start bit & stop bit for content
  High for no data/stop bit
  Low for data/start bit
Parity
  detecting errors in transmission
  extra data bit

## Slide 9: Data framing

## Slide 10: Baud-rate Introduction
What is baud-rate
  baud rate gives the frequency at which bits are transmitted on the line
Why we need baud-rate
  no clock is transmitted in asynchronous communication
  the transmitter and receiver must run independently at nearly the same baud rates
A
B
C
D
E
F
G
H
I
J
A B C D E F G I J
Transmitter :
Receiver :
A C E G I

## Slide 11: Parity Bit Introduction
What is odd/even/non parity bit
  the number of bit 1 in an word either even or odd
    even parity : we add a parity bit that number of bit 1 are even
    odd parity : we add a parity bit that number of bit 1 are odd
What is parity bit function
  UART of transmitter will calculate parity bit and send it
  UART of receiver will calculate parity bit from the data it receive
  compare two parity bit are same or not

## Slide 12
假設傳送 word : 0100 0000
odd parity bit : 0
even parity bit : 1
假設傳送word : 1111 1111
odd parity bit : 1
even parity bit : 0
Example : parity bit
Example : how to work (odd parity)
Tx
Rx
1110 0110 1

## Slide 13: UART in Pic18
EUSART mode features include
  8/9 bit mode
  Automatic baud rate detection
  Calibration
  Automatic wake-up on Sync Break reception
  12-bit Break character transmit
  No hardware parity
Notes: parity bit make 1bit even odd

## Slide 14: USART Register
Transmit Status and Control (TXSTA)
Receive Status and Control (RCSTA)
Baud Rate Control (BAUDCON)

## Slide 15: Uart init
The pins of the Enhanced USART are multiplexed with PORTC
  bit SPEN (RCSTA) must be set (= 1)
  bit TRISC<7> must be set (= 1)
  bit TRISC<6> must be set (= 1)
Uart init
  Setting baud rate(SPBRGH:SPBRG, BRGH and BRG16)
  Enable the asynchronous serial port by clearing bit SYNC and setting bit SPEN

## Slide 16: How to set Baud Rate
Baud Rate Generator (BRG)
  8-bit or 16-bit generator
The SPBRGH:SPBRG register pair controls the period of a free running timer
BRGH (TXSTA) and BRG16 (BAUDCON)
  In Asynchronous mode control the baud rate
  In Synchronous mode, BRGH is ignored
Hint: Baud setting table at data sheet

## Slide 18: EUSART TRANSMIT BLOCK DIAGRAM
Notes: The Shift register obtains its data from the Read/Write Transmit Buffer register, TXREG. The TXREG register is loaded with data in software. The TSR register is not loaded until the Stop bit has been transmitted from the previous load
如果上一次Stop bit 還沒送出去 TxReg的data不會被LOAD
Once the TXREG register transfers the data to the TSR register (occurs in one TCY), the TXREG register is empty and the TXIF flag bit (PIR1) is set
(interrupt)TXREG empty
TxREG 放入TSR後會清空 然後觸發interrupt(TXIF會立起 不論有沒有開中斷)
TXIF不能手動clear(software)
當資料load 進去TSR，只有下一個TXIF會被清空
TXIF  txreg
TRMTTSR STATUS(read only)(no interrupt)

## Slide 19: Uart init(8bit mode)
Send Data
  (If interrupts are desired, set enable bit TXIE)(init TXREG empty)
  Load data to the TXREG register (starts transmission).
  If Tsr is stop bit.Auto load TXREG and trigger interrupt(TXIF)
Hint
  TXIF cannot be cleared in software
  Status
    TXIF for TXREG
    TRMT for TSR(no interrupt)

## Slide 20: Notice TXIF
Notes: TXREG empty then TXIF set
TX busy TRMT is clear

## Slide 21: Uart init(8bit mode)
Rx Setting
  Enable the reception by setting bit CREN
  Flag bit, RCIF, will be set when reception is complete (optional interrupt)
  Reading TCTEG(you can use file register to be buffer

## Slide 22
Two level fifo
If no reading cause fifo full
The third word will cause exception
Clear CREN will make OERR clear

## Slide 23: Lab1(fix sample code)
Return word with uart from putty
  Hint

## Slide 24: Driver question
Install old driver (on moodle or web)
Update driver

## Slide 28: Lab2(add something in sample)
設計簡單指令:
  設計字串處理利用電腦下指令給Pic18
  當輸入下列字串的時候，會饋顯示給terminal並且給予相對應的動作(可以設計回應字串作Debug)(LED pin腳自行決定)
    “Control1”:亮LED1
    “Control2”:關LED1
    “Control3”:開LED2
    “Control4”:關LED2

## Slide 29: References
https://en.wikipedia.org/wiki/Asynchronous_serial_communication
https://microcontrollerpicavr.blogspot.tw/2017/08/pic-microcontroller-serial.html
http://ww1.microchip.com/downloads/en/devicedoc/39631a.pdf
https://en.wikipedia.org/wiki/Serial_port